## Slide 1: Authors: Vipin Venugopal, Ye Kuang Advisors: Dr. Bruce Land, Dr. Joseph Skovira
PIC32 and Raspberry Pi Interface
Combine real time PIC32 & powerful Raspberry Pi
Develop a cross platform system capable of performing real time tasks
Use Embedded Operating System to Enable development of software decoupled from the hardware
Implement a final application to demonstrate the system.
PIC + RPi = Real-time + Cool Linux stuff
  PIC32: Real-time input reading, analog interface and output generation
  Raspberry Pi: Linux operating system, fast decision making, higher level software, user-interface and connectivity
PIC32 PCB mates with RPi
Proof of concept: Autonomous suitcase
Built a people following robot with the system
Raspberry Pi processes vision information and controls where to go
PIC32 follows Raspberry Pi’s order and generates PWM to control motors
Best of both worlds!
RPi high speed PIC32
Raspberry Pi works as “master”, making decisions and controls PIC32, performs higher level tasks such as image processing
Pic32 works as “slave”, receiving command from Raspberry Pi and performs lower level tasks such as PWM generation
The combination of PIC32 and Raspberry Pi makes it possible for building a system with blazing fast low level functionality and a full fledged operating system
The communication protocol is universal and flexible, one can build anything with this protocol
The cost of the system is low
Command
Response
Master :
Performs higher level tasks
Slave :
Performs lower level tasks
Pi
PIC
RPi callable set of PIC32 peripheral control functions
Thanks to Dr. Bruce Land & Dr. Joseph Skovira!
Tested OK ✓
Serial Communication
PWM Generation
DAC Waveform
✔︎ Serial Comm
✔︎ PWM
✔︎ DAC Waveform
✔︎ GPIO Control
✔︎ ADC Sampling
✔︎ Data Transfer
Read input
Write output
Set Value for CHA
Set Value for CHB
Check Buffer Status
Set Sample Frequency
Start ADC
Set Period
Generate PWM 1
Generate PWM 2
Read Buffer
Write Buffer
RPi
Port Expander
DAC
RS232 Debug
Analog
PWM